## Slide 1: Medical Imaging Group Studies: Data Analysis and Image Reconstruction
Jack Joynson and Ziyue Wang

## Slide 2: Introduction
The aim of this subgroup is to generate software to reconstruct images from Compton camera data.
The image should show where the gamma ray source(s) are located.
The code has been written in C++ using Object Orientated techniques.
Notes: whether this is simulated or experimental data.
Exception is MATLAB

## Slide 3: Contents
Overview
Coincidence Checker: Calibration, Filtration and Finding coincidences
Image Reconstruction- Reading data files
Cone Generation: Theory and implication
Ellipse Generation – Conic sections and ellipse basics
Matrix Generation and plotting
Final results
Limitations
Conclusion

## Slide 4: Overview
Coincidence Finder
User input
Data calibration
Filtering
Image Reconstructor
Cone generation
Conic sections
Pixelation
Plotter
Data plotting
Fig 1 – Diagram showing the three main programs used in data analysis

## Slide 5: Coincidence Checker – Calibrating Data
The digitisers used by the experimental team output the timestamp and an uncalibrated energy of each event.
The Coincidence Checker program reads each uncalibrated energy and applies a calibration.
The timestamp can also be shifted.
Notes: The timestamp in experimental data is the 100s of picoseconds since start?
File per detector
detector specific calibration – calculated using the histogram program.

## Slide 6: Coincidence Checker – Filtering Data
The calibrated energy is checked against the user defined limits.
Valid events are stored in an ‘’ object.
Lists of ‘’ objects are created for each detector.
Notes: Greater than.. Less than..
Explain what the evententry stores?

## Slide 7: Coincidence Checker – Finding Coincidences
The events from scattering detector lists are then checked against events from absorber detector lists.
Fig 2 – Diagram showing how the event lists are checked against eachother
Notes: Each against each in pairs

## Slide 8: Coincidence Checker – Finding Coincidences
A coincidence is found when the timestamp of two events are within tolerance of each other.
Absorber events list
Scatter events list
Fig 3 – Diagram showing how pairs of event lists are checked for coincidences.
Notes: First scatter event against first absorber then iterates through absorber until finds or reaches end. Then moves on
When finds one The timestamp, energy and detector number from both events is then output to a file.

## Slide 9: Image Reconstruction - Reading Data Files
Each line of data corresponds to a coincidence.
The detector numbers are used to get the geometries from the ‘’ list which is populated by the user inputs.
The energies are used to work out the scattering angle.
Notes: The image reconstruction software has to work with simulated or experimental data processed with the ‘Coincidence checker’.
Experimental has headers which are ignored by program.
Energy provided in KeV

## Slide 10: Cone Generation
A object is produced for each coincidence.
The object defines the properties of the cone including the half angle and the image plane intersection.
We can find half angle from the rearranged Compton scattering equation where E is the total energy of the gamma ray before scatter and E is the absorbed energy.
Eq.1 Rearranged Compton scattering equation for scattering
angle in terms of total energy and absorbed energy
Notes: By the conegenerator class.
Diagram?
Explain how Compton formula used?
Trig?

## Slide 11: Conical back-projection
Fig. 4 Back projection of a
Compton scattering event,
Leading to a cone projection
with the cone having scattering
angle equal to the Compton
scatter. [1]
Generated by the “cone generator” class

## Slide 12: Detector Setup
Scattering detector
Absorbing detector
x
z
Fig. 5 Bird’s eye view of setup
dx
dz

## Slide 13: Detector Setup
Scattering detector
Absorbing detector
x
z
Fig. 5 Bird’s eye view of setup
dx
dz
Scattering rays

## Slide 14: Ellipse Generation
Fig. 6 Conic sections of the
Back-projected cones. [2]
This process is done by the “cone to
ellipse” generation class.
Notes: By the conegenerator class.

## Slide 15: Ellipse basics
Focus
Rmax
Rmin
Semi-minor axis
Semi-major axis
Fig. 7 Annotated ellipse explaining basic parameters of an ellipse.

## Slide 16: Ellipse projection onto plane
+x
-x
+y
-y
source
Fig. 8 Projection of cone plane intersection results in ellipse. Stacked ellipses result in good images.

## Slide 17: Matrix Generation
Need to know where the most ellipse intersections occur.
The program ‘draws’ each ellipse onto a matrix of pixels.
The count at each of the pixels is incremented whenever an ellipse is drawn onto it.
Intersections will naturally have a higher count than the surrounding pixels.
Notes: When saying ‘draws’ its actually just calculates the X and Y positions of the ellipse using polar coordinates and incrementing the angle.

## Slide 18: Matrix plotting
Ellipses “stack” over one another.
Point with most overlapping ellipses should be the source.

## Slide 19: Results

## Slide 20
Fig. 9 Simulation results from NaI. Midpoint is defined as 500,500 (pixels). 1 pixel = 1mm. Brightest spot (labelled) indicates
location of source. Source should be at x = 500, y = 530. 1.8cm/18 pixels off target.

## Slide 21
Fig. 10 Experimental results from NaI 2 inch scatter. Midpoint is defined as 500,500 (pixels). 1 pixel = 1mm.
Brightest spot (labelled) indicates location of source. Source should be at x = 500, y = 500. 5.1mm/5 pixels off target.

## Slide 22: Limitations
Detectors are required to be on a single plane.
Fig 11 – Diagram showing the orientation of the axes
Notes: A Compton camera being using for medical purposes would likely require the detectors to be able to move in all 3 dimensions. This complicates the mathematics blah blah.
May also have to iterate through different height slices? As in how do you work out the source distance.

## Slide 23: Limitations
More detectors should produce a better image but takes a long time to process.
Need enough events so that the random events are smeared out by the average.
Shifting the geometry of detectors due to geometric centre being different from mean scattering position.
Notes: A Compton camera being using for medical purposes would likely require the detectors to be able to move in all 3 dimensions. This complicates the mathematics blah blah.
May also have to iterate through different height slices? As in how do you work out the source distance.

## Slide 24: Uncertainties
Energy – Filtering and sum check helps to remove random events and coincidences.
Random events – Timestamp shift helps to ensure timestamps are coincident.
Finite detector size.
Uncertainties on geometric measurements.
Geometry effects image quality – how elongated ellipses are and the curvature where they overlap.

## Slide 25: Conclusion
?

## Slide 26: References
3D Image Reconstruction from Compton camera data - INSPIRE-HEP. 2018. 3D Image Reconstruction from Compton camera data - INSPIRE-HEP. [ONLINE] Available at: http://inspirehep.net/record/1446785. [Accessed 11 March 2018].
Conic section - Wikipedia. 2018. Conic section - Wikipedia. [ONLINE] Available at: https://en.wikipedia.org/wiki/Conic_section. [Accessed 11 March 2018].

## Slide 27
Focus
Source
Rmin
Rmax
Scattering detector
Absorbing detector
Fig 12. Bird’s eye view with angles labelled for derivation

## Slide 28
Focus
Rmax
Scattering detector
Absorbing detector
Rmin+dz*tan() = dx
dz
Assuming focus has coordinates (dx,0,dz)
Fig 12. Bird’s eye view with angles labelled for derivation

## Slide 29
Where a is the semi-major axis and b is the semi-minor axis