## Slide 1: Medical Imaging Group Studies: Image Reconstruction
Jack Joynson and Ziyue Wang

## Slide 2: Introduction
The aim of this subgroup is to generate software to reconstruct images from Compton camera data; whether this is simulated or experimental data.
The image should show where the gamma ray source(s) are located.
The code has been written in C++ using Object Orientated techniques.
Notes: Exception is MATLAB

## Slide 3: Overview

## Slide 4: New Overview
User Input
Data Manipulation/Calibration
Filtering
Cone generation
Conic sections
Pixelation
Plotting

## Slide 5: Coincidence Checker – Calibrating Data
The digitisers used by the experimental team output space delimited files of a timestamp and an uncalibrated energy.
The Coincidence Checker program reads each uncalibrated energy and applies a calibration.
The timestamp can also be shifted.
Notes: The timestamp in experimental data is the nanoseconds since start?
detector specific calibration – calculated using the histogram program.

## Slide 6: Coincidence Checker – Filtering Data
If the calibrated energy is within user defined limits then it is stored in an ‘’ object along with the timestamp.
Lists of ‘’ objects are created for each detector.
Explain what the evententry stores?
Notes: The timestamp in experimental data is the nanoseconds since start?
detector specific calibration – calculated using the histogram program.

## Slide 7: Coincidence Checker – Finding Coincidences
The events from scattering detector lists are then checked against events from absorber detector lists.
Diagram?
A coincidence is found when the timestamp of two events are within tolerance of each other.
The timestamp, energy and detector number from both events is then output to a file.
Notes: detector specific calibration

## Slide 8: Geometry Diagram
Shifting the geometry of detectors due to geometric centre being different from mean scattering position.
Notes: Experimental has headers which are ignored by program.
Energy provided in KeV

## Slide 9: Image Reconstruction - Reading Data Files
The image reconstruction software has to work with simulated or experimental data processed with the ‘Coincidence checker’.
Each line of data corresponds to a coincidence.
The detector numbers are used to get the geometries from the ‘’ list which is populated by the user inputs.
The energies are used to work out the scattering angle.
Notes: Experimental has headers which are ignored by program.
Energy provided in KeV

## Slide 10: Cone Generation
A object is produced for each coincidence.
The object defines the properties of the cone including the half angle and the image plane intersection.
Diagram?
Explain how Compton formula used?
Trig?
Limitations?
Notes: By the conegenerator class.

## Slide 11: Detector Setup
Scattering detector
Absorbing detector
x
z
Fig. Bird’s eye view of setup
dx
dz

## Slide 12: Conical back-projection
http://inspirehep.net/record/1446785 reference later
Fig. Back projection of a
Compton scattering event,
Leading to a cone projection
with the cone having scattering
angle equal to the Compton
scatter.

## Slide 13: Ellipse Generation
Fig. Conic sections of the
Back-projected cones.
Notes: By the conegenerator class.

## Slide 14: Ellipse basics
Focus
Rmax
Rmin
Semi-minor axis
Semi-minor axis

## Slide 15: Ellipse projection onto plane
+x
-x
+y
-y
source
Fig. Projection of cone plane intersection results in ellipse. Stacked ellipses result in good images.

## Slide 16: Matrix Generation
Need to know where the most ellipse intersections occur.
The program ‘draws’ each ellipse onto a matrix of pixels.
The count at each of the pixels is incremented whenever an ellipse is drawn onto it.
Intersections will naturally have a higher count than the surrounding pixels.
Notes: When saying ‘draws’ its actually just calculates the X and Y positions of the ellipse using polar coordinates and incrementing the angle.

## Slide 17: Matrix plotting
C# MATLAB
Surf plot – I’ll add to this tomorrow once I get the files off campus
Problem that a high density pixelation means ellipses within a small error of each other do not stack.

## Slide 18: Results
Plots
Accuracy and Precision

## Slide 19: Uncertainties
Energy – Explain filtering helps. We going to add sum check?
Random events – Timestamp shift helps +^^
Finite detector size
Geometry measurement error.
Geometry effects image quality – how elongated/overlap point etc.

## Slide 20: Limitations
Only 2D
More detectors should produce a better image but takes a long time to process.
Need enough events so average is correct.

## Slide 21: Improvements/Extensions
A Compton camera being using for medical purposes would likely require the detectors to be able to move in all 3 dimensions. This complicates the mathematics blah blah.
May also have to iterate through different height slices? As in how do you work out the source distance.